- Boot the Linux PC and login as the ‘root’ user created during Linux installation.

- On the main menus at the top left of the screen select “Applications -> System Tools -> Terminal”.

- Enter the following command to switch to the directory where the DB2 files were copied:

cd /root/Software/DB2/

- Enter the following command to begin the DB2 installation:

./db2setup

- On the window that appears click the link for “Install Products” along the left side.

- Confirm that “DB2 UDB Express” is selected to install and press the ‘Next’ button.

- On the Welcome screen press the ‘Next’ button.

- Accept the license agreement and press the ‘Next’ button.

- Select a Typical installation and press ‘Next’.

- On the screen for properties of the DB2 Administration Server user fill in and confirm a password of ‘db2admin’.  Leave the other values with the defaults and press the ‘Next’ button.

- On the screen for DB2 instance creation leave the default of “Create a DB2 instance” and press the ‘Next’ button.

- On the screen with properties of the DB2 instance owner fill in and confirm a password of ‘db2admin’.  Leave the other values with the defaults and press the ‘Next’ button.

- On the screen with properties of the fenced user fill in and confirm a password of ‘db2admin’.  Leave the other values with the defaults and press the ‘Next’ button.

- On the Summary screen press the ‘Finish’ button to begin installing the software.

- When the installation is complete, switch to the “Status report” tab and check for messages that the installation was successful.

- Press the ‘Finish’ button to close the setup wizard.

- Return to the terminal window you used to start the DB2 setup.  If you closed it you can open a new one by selecting “Applications -> System Tools -> Terminal” on the main menus at the top left of the screen.

- Enter the following command to open a text editor on the service boot configuration.

gedit /etc/inittab

- Scroll to the very bottom of the file.

- Add a ‘#’ sign to comment out the last line about the “DB2 Fault Monitor”.  The line should appear as shown below (only the beginning of the line is below).

#fmc:2345:respawn:/opt/IBM/db2/V8.1/bin/db2fmcd #DB2 Fault Monitor

- Save the file and close the editor.

- Enter the following command to open a text editor on the root user’s .bashrc file.

gedit /root/.bashrc

- Add the following lines to the bottom of the file:

#Setup DB2 Environment for root user

if [ -f /home/db2inst1/sqllib/db2profile ]; then

. /home/db2inst1/sqllib/db2profile

fi

- Save the file and close the editor.

- Enter the following command to initialize a new shell with the new DB2 environment options.

su

- Enter the following command to attempt to start the DB2 interactive command line processor.

db2

- Make sure you are able to see the “db2 =>” prompt in the command line processor to prove that the DB2 commands and libraries are available to the root user.

- Enter ‘quit’ in the DB2 command line processor to exit the tool.

- Close any windows you may have open.